## Slide 1
AI-Driven RTL to GDSII
Optimization Tool
From RTL source to a fabrication-ready GDSII layout — one dashboard, one automated pipeline, narrated by a local AI model.
Frontend: Dash · Backend: Flask + GraphQL · AI Reporting: Ollama (gemma3)

## Slide 2
The Problem, and the Fix
Today
Taking a design to silicon means running many separate EDA tools by hand — simulator, synthesizer, place-and-route, signoff checkers — each with its own commands, outputs and logs to track.
A working run and a hung one used to look identical: the browser just held an open request for minutes.
With This Tool
Design → GDSII, one path
Every stage — simulate, synthesize, place & route, sign off — chains together automatically.
One click, or one API call
Dashboard, command line, or GraphQL all run the exact same underlying flow.
Visible progress, not guessing
A live log and progress bar replace a tab that looks frozen for minutes.
AI-Driven RTL→GDSII Tool
01 Objective

## Slide 3
Three Layers, One Project
Each file has a single job — and every entry point calls the same flow underneath.
1
Frontend — dashboard.py
Dash
What the user sees and clicks. Built with Dash + dash-bootstrap-components: buttons, a progress bar and a live log, no separate HTML/CSS/JS to keep in sync.
2
Backend — app.py
Flask + GraphQL
The server. Built with Flask, exposing a GraphQL API (graphql-core); every resolver hands work off to the flow engine rather than running tools itself.
3
EDA Flow Engine — flow.py
Python + Make
The real pipeline. Runs each stage — simulate, synthesize, place & route, sign off, report — on a worker thread via flow.run_stage().
AI-Driven RTL→GDSII Tool
02 Architecture

## Slide 4
Tech Stack & Modules
What each layer is actually built on, straight from requirements.txt and the code.
Frontend
Dash
dash-bootstrap-components
matplotlib (VCD → PNG)
Backend
Flask
graphql-core
requests
AI Reporting
Ollama — model: gemma3
(local, no cloud call)
Verification
cocotb + pytest
Icarus Verilog (iverilog/vvp)
Verilator (lint)
Synthesis & Views
Yosys
Graphviz (dot)
gtkwave
Physical Design
OpenROAD (P&R)
OpenSTA (timing)
PDK: SkyWater sky130hd
sqlite3 (run history)
What's a PDK? The foundry's Process Design Kit — standard-cell libraries, Liberty timing data, LEF layout data and design rules that tie the design to real, fabricable silicon.
AI-Driven RTL→GDSII Tool
03 Tech Stack

## Slide 5
The Flow: RTL to GDSII
Six stages, one path. Every stage runs through flow.run_stage().
1
RTL Design
Generated or
uploaded
›
2
Verify
Testbench,
simulate, view
›
3
Synthesize
Map to
standard cells
›
4
Place &
Route
Place cells,
route wires
›
5
Sign-off
Timing +
physical checks
›
6
GDSII
Ready
for the fab
After Sign-off: Report + Optimize
Two more stages run after the chain finishes, reading what it measured. Neither blocks the RTL-to-GDSII path — they support it. See next slide for what Report actually generates.
AI-Driven RTL→GDSII Tool
04 EDA Flow

## Slide 6
Two Kinds of Report, One Button
Generate Report — the dashboard button, the generateReport mutation, and make report — runs both of these.
1
Flow Report
gen_report.py · deterministic
Gathers every artefact and stage summary — interface, testbench, timing, layout — into one document.
A stage that hasn't run is reported as not run; a number no tool emitted is reported as missing. Nothing is inferred.
Output: results/report/<design>_report.html + .txt
2
AI Engineering Narrative
generate_ai_report.py · Ollama, model: gemma3
Collects the actual measured outputs first, then asks a local Ollama model (gemma3) to explain them in plain English.
The model is never the source of measured numbers — it narrates what synthesis, timing and signoff already produced, and nothing else.
Output: results/report/<design>_ai_report.txt + results/ai/<design>_ai_report.json
Note — Optimize Design is a separate stage: ranked, evidence-backed advice from Yosys / OpenSTA measurements. It does not call the AI model.
AI-Driven RTL→GDSII Tool
05 Reporting

## Slide 7
One Flow, Three Interfaces
Frontend
Dash — click a stage, watch the log.
Backend
Flask + GraphQL — routes the request, tracks the job.
EDA Flow
flow.py — runs the tool, generates the AI-narrated report, reports back.
Why it matters
Whichever door you use, you get identical behavior, error handling and artifacts — the same design goes in, the same GDSII (and the same AI-narrated report) comes out. No drift between the command line, the API and the UI.